Component Model
Move to the target
Robotic Cognition System for Wheelchair
Unicamp

Table of Contents

Document Information
Project Name:	Robotic Cognition System for Wheelchair
Prepared By:	Tarcísio Franco de Carvalho	Document Version No:	1.0
Title:	Component Model – Move to the target	Document Version Date:	06/Oct/2020
Reviewed By:		Review Date:

Distribution List
From	Date	Email

Acronyms
Acronym	Description
ROS	Robot Operational System
AMCL	Adaptative Monte Carlo Localization

Document Version History
Version Number	Version Date	Revised By	Description	Filename

# Purpose of this Document
Define how the related component works and its relation in the main system.

# Component Design

## Purpose
This component is responsible to request the wheelchair robot to move to a desired target point using path planning, avoiding collisions with objects.

## System Diagram

## Component Input
This component expects the following input data:
- Current laser pan angle
- Current laser tilt angle

## Component Output
This component will move the wheelchair robot base to the target point, where it is defined in meters in x and y axis direction from the current robot position. This target point is calculated based on laser pan and tilt angle information.

## Component Processing
This component has relationship with the move_base/goal ROS node that is part of ROS navigation stack. The diagram below shows this relationship:

Below the main process flow for this component that runs in cycles:

1. Convert the laser orientation data to X and Y axis point direction
2. Set X and Y meters ahead to /move_base/goal node
3. Monitor requested action completion and return it’s status
# References

- Navigation
  - Move Base ROS: http://wiki.ros.org/move_base?distro=noetic
  - Setup in ROS: http://wiki.ros.org/navigation/Tutorials/RobotSetup
  - ROS base local planner: http://wiki.ros.org/base_local_planner
  - ROS and Gazebo Tutorial: http://wiki.ros.org/action/fullsearch/urdf/Tutorials/Using%20a%20URDF%20in%20Gazebo?action=fullsearch&context=180&value=linkto%3A%22urdf%2FTutorials%2FUsing+a+URDF+in+Gazebo%22
- Transform
  - Spherical Coordinates to Cartesian: https://www.mathworks.com/matlabcentral/answers/427558-how-can-i-create-xyz-coordinant-from-pan-tilt-system-angles
- Book - Learning Robotics using Python – Second Edition – By Lentin Joseph