Component Model
Move to target
Robotic Cognition System for Wheelchair
Unicamp

Table of Contents

Document Information
Project Name:	Robotic Cognition System for Wheelchair
Prepared By:	Tarcísio Franco de Carvalho	Document Version No:	1.0
Title:	Component Model – Move to target	Document Version Date:
Reviewed By:		Review Date:

Distribution List
From	Date	Email

Acronyms
Acronym	Description
ROS	Robot Operational System
AMCL	Adaptative Monte Carlo Localization

Document Version History
Version Number	Version Date	Revised By	Description	Filename

# Purpose of this Document
Define how the related component works and its relation in the main system.

# Component Design

## Purpose
This component is responsible to request the wheelchair robot to move to a desired target point using path planning, avoiding collisions with objects.

## System Diagram

## Component Input
This component needs the following input data:
- Current laser pan angle
- Current laser tilt angle

## Component Output
This component will move the wheelchair robot base to the target point, where it is defined in meters in x and y axis direction from the current robot position. This target point is calculated based on laser pan and tilt angle information.

## Component Processing
This component has relationship with the camera depth points ROS node, UPD library and a publisher ROS node to publish the output data. The diagram below shows this relationship:

Below the main process flow for this component that occurs in cycles:

1. Read laser scan from ROS nodelet camera depth image to laser scan parser
2. Create the environment map continuously
3. AMCL particle filter method to localize the Robotics
4. Define the path planning to a target point
5. Move to the target point
# Component Execution

To execute this component is necessary the Gazebo simulation environment, ROS main process running and the Rviz tool to show processed data. Bellow the steps to run this component:

Start Gazebo environment simulation
On the project root folder, run the script ./sim_model/scripts/launch.sh it will process the simple_blocks.world and sim_model.urdf.xacro files
Result

Start the UPD processing component
On the project root folder, run the script ./upd_run.sh it will start a node to published UPD data
Result
In Rviz the UPD data is being showing.

# References

- Navigation
  - Move Base ROS: http://wiki.ros.org/move_base?distro=noetic
  - Setup in ROS: http://wiki.ros.org/navigation/Tutorials/RobotSetup
  - ROS base local planner: http://wiki.ros.org/base_local_planner
- ROS Frame Transformation
  - http://wiki.ros.org/navigation/Tutorials/RobotSetup/TF
- FastSLAM 2.0 - http://robots.stanford.edu/papers/Montemerlo03a.html
- OpenSlam - https://openslam-org.github.io/gmapping.html
- ROS Gmapping - http://wiki.ros.org/gmapping
- ROS AMCL - http://wiki.ros.org/amcl
- Book - Learning Robotics using Python – Second Edition – By Lentin Joseph
- Open Transversability
  - UPD Home Page - http://www.maurobellone.com/robotics/upd_demo
  - UPD Git Hub - https://github.com/bellonemauro/OpenTraversability
- Point Cloud
  - Downsampling a PointCloud using a VoxelGrid filter - http://vml.sakura.ne.jp/koeda/PCL/tutorials/html/voxel_grid.html
  - Voxel - https://en.wikipedia.org/wiki/Voxel
  - Estimate the transformation matrix between two set of points (PCL): https://machinelearning1.wordpress.com/2014/02/09/estimate-the-transformation-matrix-between-two-sets-of-points-pcl/
- ROS
  - ROS and Gazebo for Depth Camera: http://gazebosim.org/tutorials/?tut=ros_depth_camera
  - Control: http://wiki.ros.org/ros_control
  - ROS and Gazebo Tutorial: http://wiki.ros.org/action/fullsearch/urdf/Tutorials/Using%20a%20URDF%20in%20Gazebo?action=fullsearch&context=180&value=linkto%3A%22urdf%2FTutorials%2FUsing+a+URDF+in+Gazebo%22
- Others
  - Rotation Matrix: https://en.wikipedia.org/wiki/Rotation_matrix
  - Rotating project point: http://www.pcl-users.org/Rotating-projected-point-cloud-to-get-z-0-for-all-points-td4034031i20.html
  - C++ Eigen Matrix: https://eigen.tuxfamily.org/dox/group__TutorialMatrixClass.html